## Slide 1: Simple Distillation

## Slide 2: Introduction
A pure liquid is recovered from a mixed solution
Specific vapor temperature of a liquid is observed
Simple distillation is effective for mixtures where vapor pressures are not close to each other.

## Slide 3: Demonstration
When the vapor temperature reaches ~78º the pure ethanol boils since the intermolecular attractions among the molecule have been broken apart and ethanol vapor travels into the condenser
The vapor condenses to pure liquid ethanol in the condenser and is collected in the receiving flask as the distillate

## Slide 4: Concepts
Distillation Apparatus
Purification of Liquids
Changes of State

## Slide 5: Distillation Apparatus
Boiling flask
Receiving
Flask
Condenser
Still Head
Thermometer
Heat
Out Water In
Boiling chip

## Slide 6: Purification of Liquids
When a solution reaches the boiling point of a constituent, the substance will vaporize.
When the vapors of the substance reach the condenser, they cool and condense into pure liquid.
The pure liquid is collected in the receiving flask until the solution stops boiling
What about Relux?

## Slide 7: Vapor Condensation
The pure liquid vaporizes at a specific temperature for the substance – the boiling point.
Cool water is run through the condenser to cool the vapor below its boiling point
A phase change is demonstrated
  Latent Heat vs Sensible Heat?

## Slide 8: Conclusions
Any mixed solutions can be purified with simple and fractional distillations
Distillation is a very important method to purify and separate liquids

## Slide 9: Comments
Rhodamine salts are a fluorescing dye and have been used in lasers.
Ethanol is a common solvent.
Boiling chips prevent “bumping” of the solution.